## Slide 1: Why digital signals are needed?

## Slide 2: Difference between analog and digital signal
Analog signals | Digital signals
Analog signals are difficult to get analysed at first. | Digital signals are easy to analyse.
Analog signals are more accurate than digital signals. | Digital signals are less accurate.
Analog signals take time to be stored. It has infinite memory. | Digital signals can be easily stored.
To record an analog signal, the technique used, preserves the original signals. | In recording digital signal, the sampled signals are taken and preserved.
There is a continuous representation of signals in analog signals. | There is a discontinuous representation of signals in digital signals.
Analog signals produce too much noise. | Digital signals do not produce noise.
Examples of analog signals are Human voice, Thermometer, Analog phones etc. | Examples of digital signals are Computers, Digital Phones, Digital pens, etc.

## Slide 3: Difference between analog and digital signal

## Slide 4
Difference between analog and digital signal

## Slide 5: Binary Logic and Gates
Binary variables take on one of two values.
Logical operators operate on binary values and binary variables.
Basic logical operators are the logic functions AND, OR and NOT.
Logic gates implement logic functions.
Boolean Algebra: a useful mathematical system for specifying and transforming logic functions.
We study Boolean algebra as a foundation for designing and analyzing digital systems!

## Slide 6: Binary Variables
Recall that the two binary values have different names:
  True/False
  On/Off
  Yes/No
  1/0
We use 1 and 0 to denote the two values.
Variable identifier examples:
  A, B, y, z, or X1 for now
  RESET, START_IT, or ADD1 later

## Slide 7: Logical Operations
The three basic logical operations are:
  AND
  OR
  NOT
AND is denoted by a dot (·).
OR is denoted by a plus (+).
NOT is denoted by an overbar ( ¯ ), a single quote mark (') after, or (~) before the variable.

## Slide 8: Notation Examples
Examples:
  is read “Y is equal to A AND B.”
  is read “z is equal to x OR y.”
  is read “X is equal to NOT A.”
Note: The statement:
  1 + 1 = 2 (read “one plus one equals two”)
is not the same as
  1 + 1 = 1 (read “1 or 1 equals 1”).
=
B
A
Y
×
y
x
z
+
=
A
X
=
In ordinary Alegbra
A + A = 2A & A.A= A2 where as in BA, A + A = A & A.A = A

## Slide 9: Operator Definitions
Operations are defined on the values "0" and "1" for each operator:
AND
0 · 0 = 0
0 · 1 = 0
1 · 0 = 0
1 · 1 = 1
OR
0 + 0 = 0
0 + 1 = 1
1 + 0 = 1
1 + 1 = 1
NOT
1
0
=
0
1
=

## Slide 10: Truth Tables
0
1
1
0
X
NOT
X
Z
=
Tabular listing of the values of a function for all possible combinations of values on its arguments
Example: Truth tables for the basic logic operations:
1
1
1
0
0
1
0
1
0
0
0
0
Z = X·Y
Y
X
AND
OR |  | 
X | Y | Z = X+Y
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 11: Truth Tables – Cont’d
Used to evaluate any logic function
Consider F(X, Y, Z) = X Y + Y Z
X | Y | Z | X Y | Y | Y Z | F = X Y + Y Z
0 | 0 | 0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 1 | 0 | 0
1 | 0 | 1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 0 | 0 | 1

## Slide 12: Logic Gate Symbols and Behavior
Logic gates have special symbols:
And waveform behavior in time as follows:
X
0
0
1
1
Y
0
1
0
1
X
·
Y
(AND)
0
0
0
1
X
+
Y
(OR)
0
1
1
1
(NOT)
X
1
1
0
0
OR gate
X
Y
Z
=
X
+
Y
X
Y
Z
=
X
·
Y
AND gate
X
Z
=
X
NOT gate or
inverter

## Slide 13: Logic Diagrams and Expressions
Boolean equations, truth tables and logic diagrams describe the same function!
Truth tables are unique, but expressions and logic diagrams are not. This gives flexibility in implementing functions.
X
Y
F
Z
Logic Diagram
Logic Equation
Z
Y
X
F
+
=
Truth Table
1
1 1 1
1
1 1 0
1
1 0 1
1
1 0 0
0
0 1 1
0
0 1 0
1
0 0 1
0
0 0 0
X Y Z
Z
Y
X
F
×
+
=

## Slide 14
Postulates of Boolean Algebra
Three basic logic operations, AND, OR & NOT
1. 0.0 = 0 6. 0 + 1 = 1
2. 0.1 = 0 7. 1 + 0 = 1
3. 1.0 = 0 8. 1 + 1 = 1
4. 1.1 = 1 9. 1 = 0
5. 0+0 = 0 10. 0 = 1

## Slide 15
Variable – is a symbol used to represent logical quantity, Any single variable can have a 1 or a 0 value.
Complement – is the inverse of a variable and is indicated by a bar over the variable, e.g., A
Literal - is a variable or the complement of a variable

## Slide 21: Commutative Laws
The commutative law of addition for two variables is written as: A+B = B+A
The commutative law of multiplication for two variables is written as: AB = BA
A
B
A+B
B
A
B+A
A
B
AB
B
A
BA

## Slide 22: Associative Laws
The associative law of addition for 3 variables is written as: A+(B+C) = (A+B)+C
The associative law of multiplication for 3 variables is written as: A(BC) = (AB)C
A
B
A+(B+C)
C
A
B
(A+B)+C
C
A
B
A(BC)
C
A
B
(AB)C
C
B+C
A+B
BC
AB

## Slide 23: Distributive Laws
The distributive law is written for 3 variables as follows: A(B+C) = AB + AC
B
C
A
B+C
A
B
C
A
X
X
AB
AC
X=A(B+C)
X=AB+AC
A+BC = (A+B) (A+C)
A + AB = A + B

## Slide 31: Additional Gates

## Slide 35: NOT gate using NAND and NOR

## Slide 39
Realization using universal gates (only NAND)

## Slide 40
Realization using universal gates (only NOR)

## Slide 42
Finding the complement of a function

## Slide 43: Canonical and standard forms
Logic function can be expressed in two forms
Sum of products (SOP)
Product of sums (POS)

## Slide 44
Canonical and standard forms

## Slide 45: Canonical and standard forms

## Slide 46
Minterms and Maxterms
A binary variable may appear in its normal form and its complement form
Four possible combinations are available for two binary variables x , y in AND operation
Each combination is called a minterm or a standard product (x’y’,x’y,xy’,xy)
For n variables 2n minterms are possible
Similarly n variables forms in OR terms with each variable being primed or unprimed
This is known are maxterms or a standard sums (x+y, x+y’, x’+y, x’+y’)

## Slide 47
Minterms and Maxterms

## Slide 48
Minterms and Maxterms

## Slide 49
Minterms and Maxterms

## Slide 50: Canonical and standard forms
Logic function can be expressed in two forms
Sum of products (SOP)
Product of sums (POS)

## Slide 51
Simplification of Boolean function using K map
A systematic method of simplification is the Karnaugh map ( ‘K map)
The map is a diagram consisting of squares
For n variables on a K map, 2n numbers of squares
Each square or cell represents one of the minterms
Boolean function can be expressed as sum of minterms
Hence it is possible to recognize the Boolean function graphically in the map from the area enclosed by those squares whose minterms appear in the function

## Slide 52
Two variable K map
Since two variable system can form four minterms, the map consists of four cells
(ie., one for each minterms)
K map for function
K map for function

## Slide 53
Three variable K map
Since eight minterms are there for three variables, the map consists of 8 cells or squares
Minterms are not arranged according to the binary sequence
Between two consecutive rows and columns only one single
Variable changes its logic from 1 to 0 or from 0 to 1

## Slide 54
Three variable K map

## Slide 55
Three variable K map

## Slide 56
Three variable K map

## Slide 57
Three variable K map

## Slide 58
Three variable K map

## Slide 59
Four variable K map

## Slide 60
Four variable K map

## Slide 61
Four variable K map
(Another way of doing this)

## Slide 62
Four variable K map

## Slide 63
Four variable K map

## Slide 64
Four variable K map

## Slide 65
Four variable K map (Examples for your reference)

## Slide 66
Four variable K map (Examples for your reference)

## Slide 67
Four variable K map (Examples for your reference)

## Slide 68
Practice Problems

## Slide 69
Practice Problems

## Slide 70
Practice Problems

## Slide 71
Examples of combinational circuits
are a half adder, full adder, magnitude comparator, multiplexer, demultiplexer, etc.
produce outputs immediately when their input changes.
Examples of sequential circuits
are flip-flop, register, counter, clocks, etc. ...
Combinational and Sequential circuits

## Slide 72
Adders
  Half adder – Addition of two binary digits
  Full adder – Addition of three binary digits
Subtractors
  Half subtractor – Subtraction of two binary digits and produce the difference
  Full subtractor - Subtraction of two binary digits taking a borrow
Combinational circuit

## Slide 73: Half adder
S – LSB
C - MSB

## Slide 74: Logic diagram of half adder
SOP

## Slide 75
Logic diagram of half adder
POS

## Slide 76
Logic diagram of half adder

## Slide 77
Logic diagram of half adder

## Slide 78
Logic diagram of half adder

## Slide 79: Full adder circuit
Full adder is a combinational circuit that forms the arithmetic sum of three binary bits
It consists of three inputs (variables) and two outputs (Sum and carry)

## Slide 80
Full adder circuit
The truth table for the full adder circuit

## Slide 81
Full adder circuit
Implementation of full adder circuit

## Slide 82
Full adder circuit
Implementation of full adder circuit with two half adders and OR gate

## Slide 83
Half subtractor is a combinational circuit, that subtract two bits and produces their difference
It performs x – y
If x >y……….
The result is ‘Difference bit’
If x<y……….
  Then ‘1’ must be borrowed from the next higher stage ‘B’ is the borrowed quantity
  The output B is 0 as long as x>=y
Subtractor – Half subtractor

## Slide 84
The Boolean expressions for the outputs of
the half subtractor can be obtained as
follows
Half subtractor

## Slide 85
Full subtractor
x-y-z

## Slide 86
Drawing the K map for the function B and D gives
Full subtractor

## Slide 87: Multiplexer

## Slide 88: Multiplexer
4 to 1 line multiplexer

## Slide 89: Demultiplexer

## Slide 90: Demultiplexer

## Slide 91: Flipflops (Sequential logic circuit)-memory elements

## Slide 92: RS flip or SR latch
Implementation using NOR gate

## Slide 93: RS flip or SR latch
Implementation using NAND gate