## Slide 1
Course Code: CS E212
Semester: III
UNIT - III
CPU control unit design: Instruction Codes - Computer Registers - Computer Instructions - Timing and Control - Instruction Cycle - Memory-Reference Instructions - Input-Output and Interrupt - Design of Basic Computer - Design of Accumulator Logic.
Microprogrammed Control: Control Memory - Address Sequencing- Microprogram Example - Design of Control Unit. Pipelining: Basic Concept - Pipeline Organization - Pipelining Issues – Data Dependencies - Memory Delays- Branch Delays - Superscalar Operation - Pipelining in CISC Processors.
Parallel Processors: Hardware Multithreading - Vector (SIMD) Processing - Cache Coherence

## Slide 2
Course Code: CS E212
Semester: III
CPU control unit design

## Slide 3
Course Code: CS E212
Semester: III
There are two major types of control organization: hardwired control and microprogrammed control.
In the hardwired organization, the control logic is implemented with gates, flip-flops, decoders, and other digital circuits. It has the advantage that it can be optimized to produce a fast mode of operation.
A hardwired control, as the name implies, requires changes in the wiring among the various components if the design has to be modified or changed.
In the microprogrammed organization, the control information is stored in a control memory. The control memory is programmed to initiate the required sequence of microoperations.
In the microprogrammed control, any required changes or modifications can be done by updating the microprogram in control memory.

## Slide 4
Course Code: CS E212
Semester: III
Instruction Codes
User of a computer can control the process by means of a program.
A program is a set of instructions that specify the operations, operands, and the processing sequence.
A computer instruction is a binary code that specifies a sequence of micro-operations for the computer.
Each computer has its unique instruction set. Instruction codes and data are stored in memory.
Computer reads each instruction from memory and places it in a control register
Control unit interprets the binary code of the instruction and proceeds to execute it by issuing a sequence of micro-operations

## Slide 5
Course Code: CS E212
Semester: III
Instruction code is a group of bits that instructs the computer to perform a specific operation (sequence of microoperations).
Operation code of an instruction is a group of bits that defines certain operations such as add, subtract, shift, and complement.
Number of bits required for the operation code depends on the total number of operations available in the computer
2n (or little less) distinct operations  n bit operation code

## Slide 6
Course Code: CS E212
Semester: III
Stored Program Organization
Instruction code is usually divided into operation code, operand address, addressing mode, etc.
Simplest way to organize a computer is to have one processor register (accumulator AC) and an instruction code format with two parts (op code, address)

## Slide 7
Course Code: CS E212
Semester: III
ADDRESSING MODES
Direct address: the address in memory of the data to use (the address of the operand)
Indirect address: the address in memory of the address in memory of the data to use

## Slide 8
Course Code: CS E212
Semester: III
COMPUTER REGISTERS
Processor has many registers to hold instructions, addresses, data, etc
Processor has a register, the Program Counter (PC) that holds the memory address of the next instruction
Since the memory in the Basic Computer only has 4096 locations, the PC only needs 12 bits
In a direct or indirect addressing, the processor needs to keep track of what locations in memory it is addressing: The Address Register (AR) is used for this and the AR is a 12 bit register in the Basic Computer
When an operand is found, using either direct or indirect addressing, it is placed in the Data Register (DR). The processor then uses this value as data for its operation
Basic Computer has a single general purpose register – the Accumulator (AC)

## Slide 9
Course Code: CS E212
Semester: III
The significance of a general purpose register is that it can be used for loading operands and storing results
  e.g. load AC with the contents of a specific memory location; store the contents of AC into a specified memory location
Often a processor will need a scratch register to store intermediate results or other temporary data; in the Basic Computer this is the Temporary Register (TR)
Basic Computer uses a very simple model of input/output (I/O) operations
Input devices are considered to send 8 bits of character data to the processor
The processor can send 8 bits of character data to output devices
Input Register (INPR) holds an 8 bit character gotten from an input device
Output Register (OUTR) holds an 8 bit character to be send to an output device

## Slide 10
Course Code: CS E212
Semester: III

## Slide 11
Course Code: CS E212
Semester: III
COMMON BUS SYSTEM
The registers in the Basic Computer are connected using a bus
This gives a savings in circuitry over complete connections between registers

## Slide 12
Course Code: CS E212
Semester: III
Three control lines, S2, S1, and S0 control which register the bus selects as its input
Either one of the registers will have its load signal activated, or the memory will have its read signal activate will determine where the data from the bus gets loaded
12-bit registers, AR and PC, have 0’s loaded onto the bus in the high order 4 bit positions
When the 8-bit register OUTR is loaded from the bus, the data comes from the low order 8 bits on the bus

## Slide 13
Course Code: CS E212
Semester: III
Computer Instructions

## Slide 14
Course Code: CS E212
Semester: III

## Slide 15
Course Code: CS E212
Semester: III
INSTRUCTION SET COMPLETENESS
Instruction Types
  Functional Instructions
  - Arithmetic, logic, and shift instructions
  - ADD, CMA, INC, CIR, CIL, AND, CLA (other than ADD/AND?)
  Transfer Instructions
  - Data transfers between the main memory and the processor registers
  - LDA, STA
  Control Instructions
  - Program sequencing and control
  - BUN, BSA, ISZ
  Input/Output Instructions
  - Input and output
  - INP, OUT

## Slide 16
Course Code: CS E212
Semester: III
CONTROL UNIT
Control unit (CU) of a processor translates from machine instructions to the control signals (for the microoperations) that implement them.
Control units are implemented in one of two ways
Hardwired Control
  CU is made up of sequential and combinational circuits to generate the control signals
Microprogrammed Control
  A control memory on the processor contains microprograms that activate the necessary control signals
We will consider a hardwired implementation of the control unit for the Basic Computer

## Slide 17
Course Code: CS E212
Semester: III
TIMING AND CONTROL

## Slide 18
Course Code: CS E212
Semester: III
TIMING SIGNALS
Generated by 4-bit sequence counter and 416 decoder
- The SC can be incremented or cleared.
- Example: T0, T1, T2, T3, T4, T0, T1, . . .
Assume: At time T4, SC is cleared to 0 if decoder output D3 is active.

## Slide 19
Course Code: CS E212
Semester: III
Basic Computer, a machine instruction is executed in the following cycle
  Fetch an instruction from memory
  Decode the instruction and calculate effective address (EA)
  Read the EA from memory if the instruction has an indirect address
  (Fetch operand)
  4. Execute the instruction
After an instruction is executed, the cycle starts again at step 1, for the next instruction
Note: Every different processor has its own (different) instruction cycle
INSTRUCTION CYCLE

## Slide 20
Course Code: CS E212
Semester: III
FETCH and DECODE
T0: AR PC (S2S1S0=010, T0=1)
T1: IR  M [AR], PC  PC + 1 (S2S1S0=111, T1=1)
T2: D0, . . . , D7  Decode IR(12-14), AR  IR(0-11), I  IR(15)

## Slide 21
Course Code: CS E212
Semester: III
DETERMINE THE TYPE OF INSTRUCTION

## Slide 22
Course Code: CS E212
Semester: III
REGISTER REFERENCE INSTRUCTIONS

## Slide 23
Course Code: CS E212
Semester: III

## Slide 24
Course Code: CS E212
Semester: III
MEMORY REFERENCE INSTRUCTIONS
Effective address of the instruction is in AR and was placed there during timing signal T2 when I = 0, or during timing signal T3 when I = 1.
  - Memory cycle is assumed to be short enough to complete in a CPU cycle
  - The execution of MR instruction starts with T4
AND to AC
D0T4: DR  M[AR] Read operand
D0T5: AC  AC  DR, SC  0 AND with AC
ADD to AC
D1T4: DR  M[AR] Read operand
D1T5: AC  AC + DR, E  Cout, SC  0 Add to AC and store carry in E

## Slide 25
Course Code: CS E212
Semester: III
MEMORY REFERENCE INSTRUCTIONS
LDA: Load to AC
D2T4: DR  M[AR]
D2T5: AC  DR, SC  0
STA: Store AC
D3T4: M[AR]  AC, SC  0
BUN: Branch Unconditionally
D4T4: PC  AR, SC  0
BSA: Branch and Save Return Address

## Slide 26
Course Code: CS E212
Semester: III
MEMORY REFERENCE INSTRUCTIONS
BSA:
D5T4: M[AR]  PC, AR  AR + 1
D5T5: PC  AR, SC  0
ISZ: Increment and Skip-if-Zero
D6T4: DR  M[AR]
D6T5: DR  DR + 1
D6T6: M[AR]  DR, if (DR = 0) then (PC  PC + 1), SC  0

## Slide 27
Course Code: CS E212
Semester: III
FLOWCHART FOR MEMORY REFERENCE INSTRUCTIONS

## Slide 28
Course Code: CS E212
Semester: III
INPUT-OUTPUT AND INTERRUPT

## Slide 29
Course Code: CS E212
Semester: III
PROGRAM CONTROLLED DATA TRANSFER

## Slide 30
Course Code: CS E212
Semester: III
INPUT-OUTPUT INSTRUCTIONS

## Slide 31
Course Code: CS E212
Semester: III

## Slide 32
Course Code: CS E212
Semester: III
PROGRAM-CONTROLLED INPUT/OUTPUT
Program-controlled I/O
Continuous CPU involvement
I/O takes valuable CPU time
- CPU slowed down to I/O speed
- Simple
- Least hardware
Input
LOOP SKI DEV
BUN LOOP
INP DEV
Output
LDA DATA
LOOP SKO DEV
BUN LOOP
OUT DEV

## Slide 33
Course Code: CS E212
Semester: III
INTERRUPT INITIATED INPUT/OUTPUT
- Open communication only when some data has to be passed --> interrupt.
- The I/O interface, instead of the CPU, monitors the I/O device.
- When the interface founds that the I/O device is ready for data transfer, it generates an interrupt request to the CPU
- Upon detecting an interrupt, the CPU stops momentarily the task it is doing, branches to the service routine to process the data transfer, and then returns to the task it was performing.
* IEN (Interrupt-enable flip-flop)
- can be set and cleared by instructions
- when cleared, the computer cannot be interrupted

## Slide 34
Course Code: CS E212
Semester: III
FLOWCHART FOR INTERRUPT CYCLE
The interrupt cycle is a HW implementation of a branch
and save return address operation.
- At the beginning of the next instruction cycle, the
instruction that is read from memory is in address 1.
- At memory address 1, the programmer must store a branch instruction
that sends the control to an interrupt service routine
- The instruction that returns the control to the original
program is "indirect BUN 0"

## Slide 35
Course Code: CS E212
Semester: III
REGISTER TRANSFER OPERATIONS IN INTERRUPT CYCLE
Register Transfer Statements for Interrupt Cycle
- R F/F  1 if IEN (FGI + FGO)T0T1T2
 T0T1T2 (IEN)(FGI + FGO): R  1
- The fetch and decode phases of the instruction cycle
must be modified Replace T0, T1, T2 with R'T0, R'T1, R'T2
- The interrupt cycle :
RT0: AR  0, TR  PC
RT1: M[AR]  TR, PC  0
RT2: PC  PC + 1, IEN  0, R  0, SC  0

## Slide 36
COMPLETE COMPUTER DESCRIPTION Flowchart of Operations

## Slide 37
COMPLETE COMPUTER DESCRIPTION Microoperations

## Slide 38
COMPLETE COMPUTER DESCRIPTION Microoperations

## Slide 39
Course Code: CS E212
Semester: III
DESIGN OF BASIC COMPUTER(BC)
Hardware Components of BC
A memory unit: 4096 x 16.
Registers:
AR, PC, DR, AC, IR, TR, OUTR, INPR, and SC
Flip-Flops(Status):
I, S, E, R, IEN, FGI, and FGO
Decoders: a 3x8 Opcode decoder
a 4x16 timing decoder
Common bus: 16 bits
Control logic gates:
Adder and Logic circuit: Connected to AC
Control Logic Gates
  - Input Controls of the nine registers
  - Read and Write Controls of memory
  - Set, Clear, or Complement Controls of the flip-flops
  - S2, S1, S0 Controls to select a register for the bus
  - AC, and Adder and Logic circuit

## Slide 40
Course Code: CS E212
Semester: III
CONTROL OF REGISTERS AND MEMORY
Address Register; AR
Scan all of the register transfer statements that change the content of AR:

## Slide 41
Course Code: CS E212
Semester: III
CONTROL OF FLAGS

## Slide 42
Course Code: CS E212
Semester: III
CONTROL OF COMMON BUS

## Slide 43
Course Code: CS E212
Semester: III
DESIGN OF ACCUMULATOR LOGIC

## Slide 44
Course Code: CS E212
Semester: III
CONTROL OF AC REGISTER

## Slide 45
Course Code: CS E212
Semester: III
ALU (Adder & Logic Circuits)