## Slide 1
Microprogrammed Control Unit
Control signals:
  Group of bits used to select paths in multiplexers, decoders, arithmetic logic units
Control variables:
  Binary variables specify microoperations
    Certain microoperations initiated while others idle
Control word:
  String of 1’s and 0’s represent control variables

## Slide 2
Control memory:
  Memory contains control words
Microinstructions:
  Control words stored in control memory
  Specify control signals for execution of microoperations
Microprogram:
  Sequence of microinstructions

## Slide 3
Control Unit Implementation

## Slide 4
Control Memory
Read-only memory (ROM)
Content of word in ROM at given address specifies microinstruction
Each computer instruction initiates series of microinstructions (microprogram) in control memory
These microinstructions generate microoperations to
  Fetch instruction from main memory
  Evaluate effective address
  Execute operation specified by instruction
  Return control to fetch phase for next instruction

## Slide 5
Microprogrammed Control Organization
Control memory
  Contains microprograms (set of microinstructions)
  Microinstruction contains
    Bits initiate microoperations
    Bits determine address of next microinstruction
Control address register (CAR)
  Specifies address of next microinstruction

## Slide 6
Microprogrammed Control Organization
  Next address generator (microprogram sequencer)
    Determines address sequence for control memory
  Microprogram sequencer functions
    Increment CAR by one
    Transfer external address into CAR
    Load initial address into CAR to start control operations

## Slide 7
Control data register (CDR)- or pipeline register
  Holds microinstruction read from control memory
  Allows execution of microoperations specified by control word simultaneously with generation of next microinstruction
Control unit can operate without CDR

## Slide 8
Microprogram Routines
Routine
  Group of microinstructions stored in control memory
Each computer instruction has its own microprogram routine to generate microoperations that execute the instruction
Subroutine
  Sequence of microinstructions used by other routines to accomplish particular task
Example
  Subroutine to generate effective address of operand for memory reference instruction
Subroutine register (SBR)
  Stores return address during subroutine call

## Slide 9
Conditional Branching
Branching from one routine to another depends on status bit conditions
Status bits provide parameter info such as
  Carry-out of adder
  Sign bit of number
  Mode bits of instruction
  I/O status condition
Info in status bits can be tested and actions initiated based on their conditions: 1 or 0
Unconditional branch
  Fix value of status bit to 1

## Slide 10
Mapping of Instruction
Each computer instruction has its own microprogram routine stored in a given location of the control memory
Mapping
  Transformation from instruction code bits to address in control memory where routine is located
Example
  Mapping 4-bit operation code to 7-bit address

## Slide 11
Address Sequencing – selection of address for control memory
Address sequencing capabilities required in control unit
  Incrementing CAR
  Unconditional or conditional branch, depending on status bit conditions
  Mapping from bits of instruction to address for control memory
  Facility for subroutine call and return

## Slide 12
Microprogram Example – Computer hardware configuration

## Slide 13
Microprogram Example

## Slide 14
Microinstruction Fields

## Slide 15
Microinstruction Fields

## Slide 16
Symbolic Microinstruction

## Slide 17
Fetch Routine
Fetch routine
  - Read instruction from memory
  - Decode instruction and update PC

## Slide 18
Symbolic Microprogram

## Slide 19
Binary Microprogram

## Slide 20
Design of Control Unit

## Slide 21
Microprogram Sequencer

## Slide 22
Input Logic for Microprogram Sequencer